Find Max in Journey
(Kickoff Coding PHP, August, 2021)

You are given three integers as an input x, y, z. You have to start a journey from the max of (x, y) and stop at min of (x, y) by taking maximum z steps. During this journey you have to find maximum value which we can get out of it.

Note:
- x, y, z >= 1
- Each step of journey can be incremented by 1 or decremented by 1 only.
- We must start from max of (x, y) and stop at min of (x, y).
- We can take max z steps, But it is not mandatory to cover all the step to reach to min of (x, y) from max of (x, y).

Test case: 6 6 4
Output: 8

Test case: 6 6 5
Output: 8

6	7	8	7	6

Test case: 6 4 8
Output: 9

Test case: 4 6 8
Output: 9

6	7	8	9	8	7	6	5	4

Test case: 6 4 5
Output: 7

6	7	6	5	4

SOLUTION

X == Y:
- (x, y, z) = (6, 6, 5)
op = x + floor(z/2)
 = 6 + floor(5/2)
 = 6 + 2
 = 8

X > Y:
- (x, y, z) = (6, 4, 8)
op = x + floor((z – (x-y)) / 2)
 = 9

X < Y:
 - Swap values and then use same formula as in X > Y